Instructions on using new libreCMC cards in a TPE-R1400 router:

0. Unplug the power to your TPE-R1400 router.

1. Push in on the microSD card currently in unit to eject old card, remove card and set aside.

2. Insert new microSD card, push in until you hear a click.

Note: Note diagram on router for how to insert the card.

3. Connect the power to your TPE-R1400 router.

After about 7 seconds the light labeled SYS on the front should start blinking, but if it does not unplug the power cable and connect it again.

4. If you do not have an ethernet cable connected between the LAN port on your TPE-R1400 router and your computer connect one now. Do the same for the WAN port, but to an upstream router with an internet connection, or modem.

5. On your computer go to the network applet and disconnect from the network. Then reconnect. It may take 1-2 minutes for the router to boot up and connect to any VPN service. If it doesn’t unplug the power and try again. Sometimes slower and lower capacity microSD cards are a bit more iffy, and can get stuck, or not boot on the first attempt, but mostly other than this they are solid and work fine for a typical router use case such as in the TPE-R1400 router.

6. Once the router has booted it’s advisable to change the router password. You can log in to the router via opening a web browser and entering https://192.168.10.1 into the web browser address bar and hitting enter. You will see a security warning message. Click the advanced button and accept/continue anyway. If your using a card with a VPN configuration on it the address will be https://192.168.3.1

Note: The default password to log in is the word ‘none’ without the quotes

To actually change the router log in password first log in and then go to System > Administration, then enter your new password twice, then click the Save button.

It’s generally a good practice to write the password down on the bottom of the router for future reference.